## Slide 1: Modeling US power grid network disruptions
Mateusz Dubaniowski

## Slide 2: Outline
Introduction – problem
Task objective
Solution
Methodology
  Network description
  Balancing methodology
  Statistics reported
Results
Summary

## Slide 3: Problem
Electricity is an important part of our lives
Used by businesses, individuals, governments…
Electrical grids consist of many various components
Potential targets of hostile attacks
Environmental conditions could have significant impact
Identifying the most critical elements of power grid systems
How we could mitigate failures of these components

## Slide 4: Task
To design and implement a network simulation of a power grid network and measure its response to node or edge failures
US power grid topology from D. J. Watts and S. H. Strogatz, Nature 393, 440-442 (1998) was used
Topology only, values of vertices and edges are randomly generated

## Slide 5: Solution
Set up a network based on the US power grid topology
Populate the network with attributes for edges and vertices
  Capacities of vertices – energy production or consumption
  Capacities of edges – transmission lines’ bandwidth
Load balance the network to make sure all capacities of vertices >0
Remove a node or an edge (or decrease capacity)
Attemptload balancing again
Present the results and various statistics about the networks

## Slide 6: Methodology – network population
US power grid network graph used is just a topology
Network needs to be populated with data about energy sources and edges capacities
We use 1/40 nodes as energy producers and randomly assign the amount produced
We use the rest as consumers, which consume 5-100 times smaller amounts
The edges are populated accordingly to be able to handle twice the average load of an edge
Each node can be theoretically discharged through connected edges

## Slide 7: Methodology – balancing the network
Network is balanced to see if it can satisfy all nodes
We average all neighboring nodes until all of them are satisfied
  Satisfied means energy available to them at the moment greater than 0
Energy exchanged between the nodes cannot exceed connecting edge’s capacity
If there is no change in subsequent steps, or maximum change in a step is very small, we determine that the network cannot be balanced

## Slide 8: Results
We present various statistics on the networks after balancing both before and after disruption
The following statistics are presented:
  Net energy value – how much energy is unused in the system
  Total energy produced
  Total energy consumed
  Average edge bandwidth – mean capacity of an edge
  Average initial min. edge bandwidth – Total energy produced/number of edges
  Extra bandwidth available in the network – Total capacity of edges – Used capacity of edges
  Edges close to or at peakBandwidth – Edges which transfer more than 90% of their capacity – these are potentially critical edges

## Slide 9: Screenshot
We also produce graph representations of the network.
Green nodes correspond to satisfied nodes
Red nodes correspond to unsatisfied with not enough electricity supplied to them nodes

## Slide 10: Results
The results could help predict for a given network whether a removal of an edge or a node would constitute a failure of the network
We can also see which edges are especially occupied in a given network i.e. which edges operate at peak bandwidth
Moreover, we we can try what is the performance of a network as edge or node capacity only decreases
This would allow us to devise more robust networks

## Slide 11: Summary
Understanding the critical points of an electrical supply network are crucial to its resiliency
We developed a simulation that predicts US power grid’s behavior when a node is removed or its capacity decreased
The approach uses load balancing of a graph as a main tool
The model run with random capacities but same topology shows that network capacities design has a big impact on network’s resiliency